## Slide 1
PowerPoint presentation
Copper pipework

## Slide 2: Joining copper pipe
  Copper has to be shaped with pipe benders and requires a high degree of skill to shape correctly. On many occasions fitting will be required to either:
  Join lengths of copper together
  Change the direction of pipework
  Add a connection
  Connect to an outlet

## Slide 3: Joining copper pipe
  Types of fitting
  The types of fittings vary according to the application but common fittings are:
  Solder
  Push-fit
  Compression

## Slide 4: Joining copper pipe
  Solder fittings
  These fittings require the copper to the cleaned, fluxed and then soldered in position. Once cooled they need cleaning to prevent corrosion. Achieving a water-tight seal is dependent on the quality of soldering.

## Slide 5: Joining copper pipe
  End-feed
  The first type of solder fitting we will look at is the end-feed fitting. The name comes from the fact that, when heated, this fitting requires solder to be fed in at the end. The solder flows into the fitting by capillary action and when cooled off creates the water-tight seal.

## Slide 6: Joining copper pipe
  End-feed components
  Tee: These allow a connection to be made to the pipework run.
  Coupling: These allow two pieces of copper tube to be connected together.

## Slide 7: Joining copper pipe
  End-feed components
  Elbow: Named after the shape of the fitting, it allows the pipework to change direction by 90º.
  Reducer: This allows the connection of a smaller diameter of pipe.
  Stop end: This is basically a cap that can seal the end of a piece of copper pipe/

## Slide 8: Joining copper pipe
  Solder ring
  These fittings are classified as non-reusable because once they have been soldered in position they cannot be moved.
  If necessary, they can however be re-heated to release the pipe from the fitting.

## Slide 9: Joining copper pipe
  Push-fit
  These fittings require care when being installed as they rely on an internal rubber O-ring to create the water-tight seal. They are simply pushed on to the copper pipe, where the grab teeth inside the fitting keep it in place.
  A square and clean-cut end to the pipe is needed to avoid damaging the O-ring.

## Slide 10: Joining copper pipe
  Push-fit
  These components are produced by many manufacturers and come in different finishes.

## Slide 11: Joining copper pipe
  Push-fit
  Tee: Coupling:
  Elbow: Reducer:
  Stop-end:

## Slide 12: Joining copper pipe
  Push-fit
  These fittings are classified as reusable because they can easily be removed with the use of a release key. The style of release key varies according to the manufacturer.

## Slide 13: Joining copper pipe
  Push-fit
  When installing these push-fit fittings onto copper pipe there is no need for the use of a sleeve or insert as the copper pipe is rigid. If they are used on plastic pressure pipe then a sleeve is required to give the pipe added rigidity.

## Slide 14: Joining copper pipe
  Compression
  These rely on a copper or brass ‘olive’ that is compressed (tightened) in position to keep the water-tight seal. Sometimes a small amount of seal paste can be used around the olive.

## Slide 15: Joining copper pipe
  Compression
  Tee: Coupling:
  Elbow: Reducer:
  Stop-end:

## Slide 16: Joining copper pipe
  Compression
  These fittings are classified as reusable because they can easily be released by the use of an adjustable spanner.
  The olive is compressed to the pipe and will need to be removed to allow the back nut to be released. A replacement olive will be required next time.

## Slide 17: Joining copper pipe
  A tap connector can be straight or bent, and solder, push-fit or compression as shown:
  The water-tight seal is achieved with the use of a small fiber washer between the tap connector and the base of the tap or float-operated valve.

## Slide 18: Joining copper pipe
  The two most common sizes for domestic pipework and fitting are:
  15mm
  22mm
  Both sizes of pipe can be purchased in 3.0m or 6.0m lengths, either in a bundle of 10 lengths or as a single length.

## Slide 19: Joining copper pipe
  Installation
  When copper pipe is installed in a property, it is required to be correctly supported to avoid any sagging or movement of the pipe, whether vertically or horizontally.

## Slide 20: Joining copper pipe
  Clipping distances
  Required clipping distances for copper pipe:

## Slide 21: Joining copper pipe
  Clips
  There are many different types of clip available for copper pipe and each is designed for use in specific situations. They all perform the same functions, however:
  To prevent sagging
  To prevent noise
  To prevent movement and damage to the pipe and fitting

## Slide 22: Joining copper pipe
  Plastic interlocking pipe clip
  This allows clips of this type to be ‘locked’ side by side.
  Plastic single push-in pipe clip
  This is used independently of other clips and is available as double clip.

## Slide 23: Joining copper pipe
  Double plastic push-in clip with saddle clips
  This is used if two pipes run in the same direction. It is also available as a single clip.
  Plastic nail-on clip
  This type is less favoured among plumbers because it can work loose. It is sometimes used under floorboards

## Slide 24: Joining copper pipe
  Copper saddle clips
  When fixing copper tubes to a skirting board, the use of copper saddle clips is recommended because it helps make the tube a little less noticeable.

## Slide 25: Joining copper pipe
  Brass school board clips
  Brass school board clips are used when installations require a more rigid fixing (for example, light commercial/industrial installations). This type of tube bracket gives more resistance to tube movement and subsequent damage.